## Slide 1
BitLinear-FPGA Alpha
Week 8 — Optimization & Benchmark Automation
Automate benchmark in one command
Separate setup / compute / readback phases
Analyze HLS unroll trade-offs
1 / 5
Erven Le Bivic · Seoul National University · LLM Core AI · 2026-06-25

## Slide 2
Week 8 — Working Artifact
Single-command execution
load-bitstream
# wait: fpga_manager state=operating
sudo ./run_benchmark.sh \
./bench_scaling \
results_week8.csv
Script checks:
fpga_manager state = operating
modprobe u-dma-buf
/dev/udmabuf0/1/2 present
Wraps CSV with timestamp + metadata
Board output (ZCU106)
=== Week 8 Benchmark (timing decomposition) ===
[ok] IP ap_ctrl=0x00000004
M K total setup compute readbk cmp%
64 128 739 253 361 125 48.9%
128 256 1773 253 1391 126 78.5%
256 512 5856 255 5471 130 93.4%
512 1024 22239 262 21845 131 98.2%
=== 8/8 PASS ===
2 / 5
Erven Le Bivic · Seoul National University · LLM Core AI · 2026-06-25

## Slide 3
Week 8 — Correctness & Timing Decomposition
8 / 8
sizes PASS
bit-exact vs CPU reference
~253 µs
T_setup (constant)
AXI writes + DMA flush
independent of matrix size
~128 µs
T_readback (constant)
sync_for_cpu
independent of output size
compute_pct = T_compute / T_total (grows with matrix size)
Chart: 
| 64×64 | 64×128 | 128×256 | 256×512 | 512×1024
Compute % | 33.9 | 48.9 | 78.5 | 93.4 | 98.2
3 / 5
Erven Le Bivic · Seoul National University · LLM Core AI · 2026-06-25

## Slide 4
Week 8 — HLS Unroll Exploration (Static Analysis)
Unroll | INNER_LOOP LUT | Total IP LUT | LUT utilization | Est. GOPS | DDR BW (MB/s)
×1 (current) | 850 | 4 378 | 1.90 % | 0.048 | 25
×2 | ~1 700 | ~5 228 | 2.27 % | ~0.096 | 50
×4 ← recommended | ~3 400 | ~6 928 | 3.01 % | ~0.192 | 100
×8 | ~6 800 | ~10 328 | 4.48 % | ~0.384 | 200
×16 | ~13 600 | ~17 128 | 7.43 % | ~0.768 | 400
×32 | ~27 200 | ~30 728 | 13.3 % | ~1.536 | 800
LUT headroom
Even at ×32, utilization < 14 %
LUT budget is not the constraint
DDR bottleneck
HP port ~3 GB/s burst → ceiling ~50–60
usable parallel lanes
0 DSP used
Ternary {−1, 0, +1} needs no multiplier
Add/sub maps to pure LUT logic
4 / 5
Erven Le Bivic · Seoul National University · LLM Core AI · 2026-06-25

## Slide 5
Week 9 — What will be demonstrated
ASIC Scaling Note
Explain how the FPGA IP core becomes future ASIC IP.
Compare FPGA limitations vs. ASIC opportunities.
Estimate what changes at ×4 unroll on a larger device.
Architecture Diagram
System diagram: PS ↔ PL ↔ DDR4 data flow.
Annotated with measured latency breakdown.
Final Report Draft
erven_fpga_report_draft.md committed to repo.
Full narrative: Week 1 → Week 9 arc.
Demo Video Draft
Short screen recording: board boot → benchmark → CSV.
No live debugging — reproducible from run_benchmark.sh.
5 / 5
Erven Le Bivic · Seoul National University · LLM Core AI · 2026-06-25